## Slide 1: CHARACTERISTICS OF ATMOSPHERIC AEROSOL IN URBAN AND SUB-URBAN AREA OF CENTRAL BALKAN
Dragana Đorđević1 and Andrea Gambaro2,3
1Centre of Excellence in Environmental Chemistry and Engineering,
ICTM - University of Belgrade, Institute of National Importance for Republic of Serbia
Njegoševa 12, 11000 Belgrade, SERBIA
Studentski trg 12 – 16, 11001 Belgrade, SERBIA
dragadj@chem.bg.ac.rs
2Department of Environmental Sciences, Informatics and Statistics, University Ca' Foscari of Venice, Dorsoduro 2137, 30123 Venice, Italy.
3Institute for the Dynamics of Environmental Processes National Research Council (CNR-IDPA), Dorsoduro 2137, 30123 Venice, Italy.

## Slide 2
An atmospheric aerosol seldom consists of a single component - it is a mixture of species from a number of sources:
  natural and
  anthropogenic.
Particles have various atmospheric lifetimes because of various particles sizes and their complex chemical composition.
Fine particles are of especially importance because of their:
  impact on human health,
  ability to scatter light affecting visibility, and
  role in global climate change.

## Slide 3
Mihajlidi-Zelić et al, Central European Journal of Chemistry

## Slide 4
The sampling sites (44049’N, 20027’E) urban and suburban areas in Belgrade.

## Slide 5
Size segregated aerosol samples collected using High Volume Cascade Impactors

## Slide 10
Characteristics of ambient air aerosol – Belgrade
Urban atmosphere of Belgrade
Đorđević et al., 2012, Atmospheric Environment 48 309-317

## Slide 11
Sub-urban atmosphere of Belgrade
The dominant aerosol fraction is between 0.50mm and 1.0mm
Đuričić-Milanković et al., 2018, Environmental Science and Pollution Research

## Slide 12
Đorđević et al., 2012. Atmospheric Environment, 46, 309-317

## Slide 13
Jelena Đuričić-Milanković et al., 2018, Environmental Science and Pollution Research

## Slide 14
07 – 09 September 2008 (SW) |  |  |  |  |  |  | 
Al/Si | 0.50 | Ca/Si | 0.24 | K/Si | 0.13 | Fe/Si | 0.26
Mg/Si | 0.12 | Ni/Si | 0.15 | S/Si | 0.06 | P/Si | 1.08
Ca/Al | 0.40 | Si/Al | 2.10 | Fe/Ca | 0.40 | K/Ca | 0.50
Mg/Na | 2.00 |  |  |  |  |  | 
13 – 15 October 2008 (NW) |  |  |  |  |  |  | 
Al/Si | 0.27 | Ca/Si | 0.48 | K/Si | 0.26 | Fe/Si | 1.36
Mo/Si | 2.47 | Ca/Al | 1.81 | Si/Al | 3.77 | Fe/Ca | 2.81
K/Ca | 0.54 | Mo/Fe | 1.82 |  |  |  | 
06 – 08 November 2008 (SE) |  |  |  |  |  |  | 
Al/Si | 0.41 | Ca/Si | 12.16 | K/Si | 0.08 | Fe/Si | 0.55
As/Fe | 0.52 | As/Si | 0.05 | Br/Si | 1.09 | Si/Al | 2.37
Zn/Si | 0.02 | Zn/Fe | 0.27 | Ca/Al | 1.04 | Sn/Zn | 2.95
Fe/Ca | 0.01 | K/Ca | 0.93 | Mg/Si | 0.07 |  | 
18 – 20 November 2008 (N) |  |  |  |  |  |  | 
Al/Si | 0.28 | Ca/Si | 0.95 | K/Si | 0.23 | Fe/Si | 0.54
As/Fe | 0.13 | As/Si | 0.02 | Ca/Al | 0.83 | Fe/V | 5.44
K/Ca | 1.78 | Mg/Si | 0.08 |  |  |  | 
Đorđević et al. 2014, Environmental Science and Pollution Research
Energy dispersive X-ray (EDX) analysis

## Slide 15
Đorđević et al. 2018, in press
Elements ratio in suburban atmospheric aerosols of central Balkans’ corresponding with their ratios in surface crustal material of Northern Africa for air masses coming from Northern Africa
 |  | Characteristic elements ratios |  |  |  |  |  | 
Periods | Air masses | Ca/Al | K/Al | Fe/Al | Mg/Al | Mn/Al | Ca/Fe | Mg/Fe
1st – 3rd April 2012 | SW | 3.48 |  |  |  |  | 1.57 | 0.26
4th – 6th April 2012 | S |  | 0.50 | 1.15 | 0.36 | 0.03 | 1.50 | 0.35
24th – 26th August 2012 | SW |  |  | 1.21 | 0.45 | 0.03 | 2.25 | 0.34
17th – 19th October 2012 | SW |  |  | 1.07 |  | 0.03 |  | 0.52
10th – 12th November 2012 | SW |  |  | 1.22 |  | 0.04 |  | 0.90
4th – 6th March 2013 | SW | 0.51 | 0.22 | 0.89 | 0.39 | 0.03 |  | 0.47
16th – 18th March 2013 | SW | 0.49 |  |  |  |  |  | 0.22
3rd – 5th April 2013 | SW |  | 0.10 | 1.20 | 0.37 | 0.03 | 0.40 | 0.20
21st – 23rd April 2013 | SW | 0.35 |  | 0.75 | 0.29 |  | 0.49 | 0.37
27th – 29th April 2013 | SW | 0.31 | 0.45 |  | 0.26 |  | 0.48 | 0.38
15th – 17th May 2013 | S | 0.56 |  |  | 0.31 |  |  | 0.44
27th – 29th May 2013 | S | 0.61 |  |  | 0.51 | 0.03 |  | 0.27
8th – 10th June 2013 | SW | 0.59 |  | 0.98 | 0.31 |  | 2.75 | 0.48
6th – 8th October 2013 | S | 0.31 | 0.29 |  | 0.74 |  |  | 0.13
12th – 14th October 2013 | SW | 1.86 | 0.30 |  | 0.77 | 0.04 | 2.03 | 0.27
17th – 19th November 2013 | S | 7.59 |  |  |  |  | 1.18 | 0.23
24th – 26th December 2013 | S | 2.18 |  |  |  |  | 0.98 | 0.48

## Slide 16
Đorđević et al. 2019, in press
Element ratios in suburban atmospheric aerosols of central Balkans’ corresponding with volcanic soil in South Iceland
 |  | Characteristic elements ratios |  |  |  |  | 
Periods | Air masses | Ca/Al | Mg/Al | Fe/Al | Mn/Al | Ca/Fe | Mg/Fe
6 – 8th August 2012 | NW | 1.01 | 0.39 | 1.46 | 0.03 | 0.42 | 0.31
26th – 28th June 2013 | NW | 0.90 | 0.32 | 1.06 | 0.02 | 0.39 | 0.31
18th – 20th September 2013 | NW |  | 0.47 | 1.72 | 0.08 |  | 0.35

## Slide 18
Đorđević et al. 2014, Environmental Science and Pollution Research 21:10949–10959
Urban atmosphere
The dominant share of the mean values of the nucleation mode is found for: As, K, Ni, V and U
pointing to anthropogenic emission sources: traffic, heating, combustion processes

## Slide 19
Jelena Đuričić-Milanković et al., in press
Suburban atmosphere
The dominant share of the mean values of the nucleation mode is found for: As, Cd, K, Pb and V
pointing to anthropogenic emission sources

## Slide 20
Đorđević et al., 2012, Atmospheric Environment 48 309-317
The absolute highest concentration was found for SO42– (1555.8 ± 973.6 ng m–3, i.e., 8.19 % of the total aerosol mass) in the particle size range Dp < 0.49 mm,
The formation of (NH4)2SO4 was found to be the dominant process, indicating the combustion of fossil fuels enriched with sulfur.

## Slide 21
Đorđević et al., in press
Among atmospheric particles of urban atmosphere in Belgrade - spheric silicate skeletons (Cenospheres) have found.
Cenospheres are tracers for high temperature combustion of coal where they form.

## Slide 22
Carbon cenosphere adsorbed by ultrafine particles
Đorđević et al., ESPR

## Slide 23
Đorđević et al., 2016, Environmental Science and Pollution Research, 23(1)851-859
Soot enriched with As in urban atmosphere of Belgrade indicating lignite combustion

## Slide 24
Đorđević et al., in press
Data set of As concentration have tested with corresponding expected and observed cumulative probabilities by next distributions:
normal,
log-normal and
Weibull
As in the fine particles showed the best fitting with the log-normal test cumulative probability indicating local and regional emission sources of As.

## Slide 25
Over 70% of the electricity in Serbia comes from Coal Fired Power Plants (CFPPs)
There are six CFPPs which use low caloric coal - lignite as a fuel.
CFPP are located in the vicinity of the main lignite deposits of Kolubara and Kostolac basins.
32.000.000t/year of lignite is burning and generate 6.000.000t/year of ash.
Combustion temperature of the coal are around 20000C and can be higher.

## Slide 26
Characteristics of lignite used in Coal Fired Power Plants (CFPP) in Serbia
General characteristics of Kolubars’ and Kostolacs’ lignite are:
- low caloric value – three times lower than average: 6200-8600 kJ/kg
- 10-26% fly ash
- 45-52% humidity
- 0.3-0.8% sulfur
Lignite contains As, Be, Co, Cr, Mo, Mn, Ni, Pb, Se, Sb and V and concentrate significant contents of elements in ash.
About 1.4g of As and 0.4g of Hg as a gas are emitting during combustion 1t of Kolubaras’ lignite.
In addition, lignite contains U, Th, Ra and Rn. All quantity of Rn from the combustion are emitting as a gas.
Elements in the vapor are more dangerous than one in particles.
Diameter of emitted fly ash particles correspond to PM10, dlp= 10 μm (respirable).
The emission of pollutants from the burning cause environmental and health problems.

## Slide 27
 | Installed power (MW) | Coal consump. (t/h) | Block | Eff. of electrofilt. (%) | Humid gas velocity (m3/h) | Particles conc. (mg/m3) | Particle emiss. (t/year)
TENT A1 | 210 | 260 | 7.290 | 97,12 | 1.303.000 | 796 | 10.905
TENT A2 | 210 | 265 | 3.342 | 95,10 | 1.269.000 | 1.429 | 8.675
TENT A3 | 305 | 369 | 7.411 | 99,75 | 1.727.000 | 78 | 1.360
TENT A4 | 308,5 | 353 | 6.669 | 99,78 | 1.533.000 | 138 | 1.028
TENT A5 | 308,5 | 370 | 4.698 | 99,79 | 1.608.000 | 105 | 725
TENT A6 | 308,5 | 336 | 1.747 | 99,00 | 1.867.000 | 300 | 1.172
TENT B1 | 620 | 754 | 7.756 | 99,62 | 3.184.000 | 111 | 4.460
TENT B2 | 620 | 762 | 8.159 | 99,73 | 3.293.000 | 71 | 3.366
Characteristics of CFPPs utilities of »Nikola Tesla A« and »Nikola Tesla B« and of particles emissions, according to measurements
D.M. KISIĆ et al., Hem. ind. 67 (5) 729–738 (2013)
Electrofilters are of limitted efficiency; first of all for soot and for Zn, Mn and Pb in fly ash.

## Slide 28
Threats to surface and underground water pollution come from lignite ash
Cr (around 6 t/year), 1.5 t of Zn, and between 600 and 700 kg of Ni, are
being leached each year from ash due to transport processes to ash disposals .
(Popović et al., 2001, Environment International, 26(4)251-255)
The largest fraction of elements were associated with the mobile forms.
(Popović and Đorđević, 2005, J. Serb. Chem. Soc. 70(12)1497-1513)
The influence of CFPPs Kostolac and Drmno on the quality of ground water springs is noticed.
The delayed impact has Co from draining waters, Cr and Si from owerflow waters and Mg and V from both overfolow and drainage waters.
(Popović et al., 2007, Fuel, 86 218-226)
The most recently deposited ash represents the highest environmental threat.
(Popović and Đorđević, Energy Sources, Part A: Recovery, Utilization, and Environmental Effects, 31(17) 1553-1560)
(Popović and Đorđević, Energy Sources, Part A: Recovery, Utilization, and Environmental Effects, 37(11) 1224-1232)
(Popović and Đorđević, Energy Sources, Part A: Recovery, Utilization, and Environmental Effects, 37(12) 1291-1299)

## Slide 29
On 2nd May 2018th World Health Organisation (WHO) issued document
Ambient (outdoor) air quality and health with some key facts:
Air pollution is a major environmental risk to health:
heart disease,
lung cancer,
and both chronic and acute respiratory diseases, including asthma.
Ambient (outdoor) air pollution in both cities and rural areas was estimated to cause 4.2 million premature deaths worldwide in 2016.
According to toxicological profiles next elements: Al, As, Cd, Co, Cr, Mn, Ni, Pb, Sb, U and V in atmospheric aerosols were identified to have toxicological effects on human health.
The carcinogenic risk has calculated by EPA methodology (US EPA 2013; US EPA 2015), equation below was used:
R = EC × IUR
where is:
R is carcinogenic risks
EC exposure concentration (mg m-3)
IUR - inhalation unit risk

## Slide 30
Unpublished data
Non-carcinogen hazard quotients (HQ) and carcinogen risks (R) in total PM a) and b), and in PM<0.49 c) and d)
Regional population is under high carcinogenic risk due to high quantities of As and Cr in the respirable atmospheric aerosols

## Slide 31
Instead of conclusion
Serbia has many other possibilities for clean and low carbon energy production:
biogas production from biomass with which Serbia is one of the richest
countries,
metain production from farms and waste dispolsal and its use for
energy production,
huge potential of geothermal energy,
wind energy,
solar energy, etc.
The most important approach must be towards energy efficiency in all sectors:
Cogeneration and energy save in industry,
Energy efficiency in public and domestic sector

## Slide 32
Thank you for your attention!